Policing Drones
By:-
Jayeshkumar Patel
EECE5698
Northeastern University

---
Power Bus
- Voltage regulators/Power Distribution Board(BEC or UBEC): To provide regulated voltages to FPV and other sensors and devices (Also providing isolation between motors and other sensors and devices.)
- Electronic Speed Control: To generate three phase signals to operate brushless dc motors and its speed control based on PWM input signal.(may have an in-built voltage regulator)
- LiPo Battery: Mostly used because of its high power to weight ratio. Extra care needed to charge and maintaining its charge levels to avoid degradation.(Capacity to be determined)

---
Sensors
- FPV camera: To look at the scene in front of the drone. (An OSD module may be included to obtain additional information such as battery level,etc.)
- Ultrasonic sensors: For possible collision avoidance/detection from the rest of the sides.

---
Navigation
- GPS: To determine position of the drone. (Activated only when needed in situations such as low battery power and auto-homing to charging station, or when its current location needs to be determined,etc.)
- IMU: Needed to stabilize the drone by receiving feedback on its orientation.

---
System architecture