GPS Device Analysis
 By:-
Jayesh Patel
EECE5698
  Northeastern University

---
Stationary Readings and Analysis

---
Error Analysis
- It can be seen from the stationary readings and their accuracy mesurements in the previous slide that error distribution is non-uniform.
- As the true values of utm co-ordinates are unknown, their average values are used for calculation of standard deviation. These std_deviation values are used to calculate GPS accuracy measures such as CEP (circular error probable) and 2DRMS values. (shown in previous slide)
- GPS location for a stationary object is affected by several factors and hence the probable area for its position is quite large compared to that for a moving object.
Blue circle --> 2DRMS
Green circle --> CEP

---
Straight Path Readings
- It is evident that GPS accuracy improves for a moving object.
- The position errors for a moving object are reduced quite a lot compared to that of a stationary object.
- This is due to the reduction of intersection area of the locating spheres while moving.